## Slide 1: RADIG: Resolution-Adaptive Digit Interleaving Grid for multi-resolution grid index
Sheng Zhou
Senior Data Scientist
Data Science & Analytics
Chief Geospatial Office
Ordnance Survey

## Slide 2: BNG grid reference as a spatial indexing method
Easy to interpret (by human) and efficient
Fundamental issues:
Fixed resolution for all features in a dataset
  Huge challenge on selecting an appropriate resolution for dataset with vast feature size variation
Two datasets to be joined have to be indexed at the same resolution

## Slide 3: Resolution-Adaptive Digit Interleaving Grid (RADIG)
A framework to tackle the multi-resolution grid reference problem
References at different resolutions in the same dataset
Mixed resolution references for the same feature
Joining two datasets with references at mixed resolutions (provided they are indexed under the same RADIG)
Using Digit Interleaving encoding to represent resolution hierarchy in reference string

## Slide 4: Digit Interleaving: BNG vs RADIG as a practical example
A sample BNG coordinate: 562356, 231722
BNG Grid references at different resolution (interleaving + concatenation) : TL->TL63->TL6231->TL623317-> TL62353172->TL6235671322
RADIG aligned to BNG and using digit interleaving encoding: TL->TL63->TL6321->TL632137->TL63213752->TL6321375262
Digit Interleaving: 5 6 2 3 5 6, 2 3 1 7 2 2 Digit Concat: 5 6 2 3 5 6, 2 3 1 7 2 2
RADIG Ref: T L 6 3 2 1 3 7 5 2 6 2 BNG Ref: T L 6 2 3 5 6 3 1 7 2 2

## Slide 5: Digit Interleaved RADIG Reference for Multi-Resolution Process
Grid cell hierarchy represented by the order of digits in digit interleaving references:
Ref Series for (562356, 231722): TL->TL63->TL6321->TL632137->TL63213752->TL6321375262
  Grid_Cell(TL).contains(Grid_Cell(TL63)) <=> “TL63”.startsWith(“TL”) == True
  Grid_Cell(TL63).contains(Grid_Cell(TL6321) <=> “TL6321”.startsWith(“TL63”) == True
  And so on…
Original BNG: TL63 vs TL6231 (not sub-stringing)
TL63
TL6321

## Slide 6: Grid Cell Containment/Intersection by Substring Operations
Containment
containDF = dfFeat.join(dfQry, dfFeat.RadigRef.startsWith(dfQry.RadigRef))
Intersection
interDF = df1.join(df2, df1.RadigRef.startsWith(df2.RadigRef) | df2.RadigRef.startsWith(df1.RadigRef))

## Slide 7: Sub-stringing: Performance Issue
StartsWith()
  Many DBMS don’t have it
  Some have it, but not optimised
    In Spark SQL, the call is translated to a cross-join

## Slide 8: RADIG Prefix Matching
BNG References Matching
String comparison, merge-sort, efficient
RADIG Reference Matching
May be performed using standard SQL query
Prefix matching, not necessarily optimised in all DBMS and may have performance issue
Potential solution: Multi-way Trie (Prefix tree) index for RADIG reference values
  Example: TL6321375262
T
L
6
3
2
1
3
7
5
2
6
2
M
G
…
…
7
5
…
…
4
2
…
…
3
1
…
…
2
0
…
…
4
2
…
…
8
6
…
…
6
4
…
…
3
1
…
…
7
5
…
…
3
1
…
…
U
…
…
S

## Slide 9: RADIG Match Trie
Given query reference TL6321
Drill down from top of the Trie per digit
First matching node (red cycle) and all its children (inside the dashed box) are the result
Joining two RADIG Match Tries:
Synchronised traversal
Traverse on one Trie, visit corresponding node on the other
Time complexity: O(amN) (a: the ave. key length; m: the alphabet size; N : the max Trie size)
T
L
6
3
2
1
3
7
5
2
6
2
M
G
…
…
7
5
…
…
4
2
…
…
3
1
…
…
2
0
…
…
4
2
…
…
8
6
…
…
6
4
…
…
3
1
…
…
7
5
…
…
3
1
…
…
U
…
…
S

## Slide 10: Scalable RADIG Match Trie
Partition and Conquer: two approaches
Partition by object keys
Partition of key space

## Slide 11: RADIG Prefix Matching (3)
On distributed systems such as Spark in Databricks
Partition Scheme:
  Regular Grid (simple, good for evenly distributed data)
  RADIG Partition Trie (Adaptive to data distribution, more complicated, may have no gain?)
Matching:
  RADIG Match Trie: efficient, needs more memory
  RADIG Reference SubStringing: simple, but not as efficient

## Slide 12: Dynamic Generation of Grid References Adaptive to Feature Extent
Polygon feature as an example
Start at a large resolution (equal or larger than the extent of the feature)
Test “effective area” value (proportion of cell intersecting the feature)
If ratio higher than predefined threshold, return the reference of this grid cell
Otherwise, sub-divide the cell, goes to next finer resolution to repeat the test
Also controlled by a cut-off minimum resolution, and a maximum levels of sub-division

## Slide 13: Flow Chart for RADIG Reference Generation
Pure digit-string output
BNG-style as a customised instance
Support encoding in different radix number systems (e.g. base10, 2, 8, 16)
Currently implemented in Java, with Scala wrappers for Databricks
Further details in the technical report
Encoding prefix
Dual Divisors to improve resolution granularity and support the 5x tiles
geometry
Grid Spec.
(G, B, I, D)
Acquire Initial Resolution and generate RADIG
Test Cell-geometry intersection
Intersects?
Compute EA/EL
Above threshold or reach level/res limit
Recycle cell
Cell sub-division
Output reference
Result

## Slide 14: Mosaic vs RADIG: Space Utilisation
 | Parameter | Reference count | Total grid cell aera | Largest cell edge length
BNG (Mosaic) | Optimal Res = -6(5.0m) | 66238 | 1652230.0 | 5
BNGRadig | DivLevel = 15, minRes = 5.0, ea = 0.5 | 38281 | 1725418.0 | 100
BNGRadig | DivLevel = 15, minRes = 5.0, ea = 0.8 | 50993 | 1653578.0 | 50
BNGRadig | DivLevel = 15, minRes=5.0, ea = 1.0 | 58932 | 1652328.0 | 50
Sample data: Topobase landformArea (30km x 30km) with 1190 features

## Slide 15: Mosaic vs RADIG: Running Time
Dataset: 40298590 address points vs 14767492 building polygons (Z-Order optimised when applicable)
 | time | Note 1 | Note 2
Mosaic | 1.81min |  | 
RADIG Match Trie | 4.51min |  | 
RADIG Ref SubStringing | 3.36min | One-way match | Only applicable for point-in-polygon
RADIG Ref SubStringing | 10.9min | Two-way match | 

## Slide 16: Sample RADIG Outputs (1)
Base-10, 2 divisors (2X5), max level 4, area ratio 0.8
Base-10, divisor 2x5, max level 4, area ratio 0.8, containing cells are separated

## Slide 17: Sample RADIG Outputs (2)
Base-10, max level 5, 2x5 divisor
Base-16, max level 4, 4x4 divisors
Base-2, max level 6